## Slide 1: Basic Packages
Focus is on the following 4 packages:
  River (RIV) Package →
  Streamflow Routing (SFR) Package
  Recharge (RCH) Package →
  Unsaturated Zone Flow (UZF) Package
  Well (WEL) Package →
  Multi-Aquifer Well (MAW) Package
  High K Lake Cells →
  Lake (LAK) Package
“h”: head in the cell

## Slide 2: Advanced Stress Packages
Include
  Lake (LAK)
  Streamflow Routing (SFR)
  Multi-Aquifer Well (MAW)
  Unsaturated Zone Flow (UZF)
  Mover (MVR)
Typically involve solving some form of a water budget equation
  As part of the formulation step (LAK, SFR, UZF, MVR)
  Added as rows in the system of equations solved (MAW)

## Slide 3: River (RIV) Package

## Slide 4: RIV Package Notes
Water is added to or removed from individual cells
There is no concept of routing and therefore no dynamic simulation of streamflow
May want to ignore short reaches
Can use the budget table to assess groundwater/surface-water exchanges

## Slide 5: RIV Package Conductance:

## Slide 6
Streamflow Routing (SFR) Package
Streamflow is routed in one direction only
Groundwater/surface-water exchanges either add to or subtract from streamflow
Carries a much bigger parameterization requirement (see below)

## Slide 7
BEGIN OPTIONS
END OPTIONS
BEGIN DIMENSIONS
END DIMENSIONS
BEGIN PACKAGEDATA
END PACKAGEDATA
BEGIN CROSSSECTIONS
END CROSSSECTIONS
BEGIN CONNECTIONDATA
END CONNECTIONDATA
BEGIN DIVERSIONS
END DIVERSIONS
BEGIN INITIALSTAGES
END INITIALSTAGES
BEGIN PERIOD <iper>
END PERIOD <iper>
Streamflow Routing (SFR) Package
SFR input blocks

## Slide 8
Streamflow is routed in one direction only
Groundwater/surface-water exchanges either add to or subtract from streamflow
A bigger parameterization requirement
Stream networks can be established through connections:
Reach: Connections:
-2
1 -3
2 -4 -16
3 2 -16 (alternative)
…
13 9 12 -14
Streamflow Routing (SFR) Package

## Slide 9
Streamflow is routed in one direction only
Groundwater/surface-water exchanges either add to or subtract from streamflow
A bigger parameterization requirement
Stream networks can be established through connections
Streamflow Routing (SFR) Package
“3 1 4 FRACTION”

## Slide 10
Stress Period Data:
Streamflow Routing (SFR) Package

## Slide 11
Streamflow Routing (SFR) Package

## Slide 12
Intended for basin scale studies
Numerically stable
Simulates
Gravity flow in the unsaturated zone
Evapotranspiration (unsaturated and saturated)
Infiltration excess (rejected infiltration)
Saturation excess (groundwater discharge to land surface)
Unsaturated Zone Flow (UZF) Package

## Slide 13
Recharge
Unsaturated Zone Flow Package
Specified
Specified
Runoff
DS
Calculated
ET
Unsaturated Zone Flow (UZF) Package

## Slide 14
Unsaturated Zone Flow (UZF) Package
1
2
3
6
5
4
7
8
9
16
17
18
18
15
12

## Slide 15
Capabilities
Solved as part of the matrix solution
Simplified data input
Flexible connectivity
Several well conductance formulations
Constraints (flow reduction and well shutdown)
Flowing well option
Can account for interbore storage changes
Constant and inactive wells
Differences
No support for
  horizontal wells
  partial penetration
  non-linear head losses
Multi-Aquifer Well (MAW) Package

## Slide 16
Capabilities
Solved as part of the matrix solution
Simplified data input (compared to MNW)
Flexible connectivity
Several well conductance formulations
Constraints (flow reduction and well shutdown)
Flowing well option
Can account for interbore storage changes
Constant and inactive wells
Differences
No support for
Multi-Aquifer Well (MAW) Package

## Slide 17
BEGIN OPTIONS
END OPTIONS
BEGIN DIMENSIONS
END DIMENSIONS
BEGIN PACKAGEDATA
END PACKAGEDATA
BEGIN CONNECTIONDATA
END CONNECTIONDATA
BEGIN ANGLEDATA
END ANGLEDATA
BEGIN PERIOD <iper>
END PERIOD <iper>
MAW input blocks
Multi-Aquifer Well (MAW) Package

## Slide 18
Multi-Aquifer Well (MAW) Package

## Slide 19
Multiple outlets per lake using 3 outlet equation options (specified, Manning, weir)
Lake (LAK) Package
Lakes sit on top of model grid (overlying), incised lakes, embedded lakes (sub-grid scale lakes)
Constant stage and inactive lakes
Explicitly defined lake connectivity
Currently no UZF under lakes

## Slide 20
Lake (LAK) Package

## Slide 21
Lake (LAK) Package

## Slide 22
Mover (MVR) Package
https://doi.org/10.1111/gwat.13117

## Slide 23
Package
Discharge
RECEIVER
PROVIDER
CONSTRAINTS
Receiver 2
Receiver 3
Provider 1
Receiver 1
One to One
Provider 2
One to Many
Provider 3
Provider 4
Many to One
Receiver 4
Mover (MVR) Package

## Slide 24: MVR Package Providers and Receivers
Providers
  Drain package
  General-head boundary package
  River package
  Well package
Provider and Receiver
  Lake package
  Multi-aquifer well package
  Streamflow routing package
  Unsaturated zone package
    Water that is made available to the mover by a single provider and is subsequently allocated to multiple receivers is allocated in the order listed in Mover package

## Slide 25: MVR Package Providers and Receivers
Similar to options available for CPRIOR in the SFR Package
1) Fraction
  Discharge x fraction is sent to the receiver
2) Excess
  Any water that exceeds the user-specified rate is provided to the receiver. No water is provided to the receiver if the available water is less than the user-specified value. (Flood control)

## Slide 26: MVR Package Providers and Receivers
3) Threshold
  No flow is provided to the receiver until the available water exceeds the user-specified rate. Once the available water exceeds the user-specified rate, then the user-specified rate is provided to the receiver. (Priority)
4) Up To
  All of the available water will be taken from the provider up to the user-specified rate. Once user-specified rate is exceeded, the receiver will continue to get the user-specified rate.

## Slide 27: Example Use Cases of MVR

## Slide 28: MVR examples
#

## Slide 29: More MVR Examples
#

## Slide 30: MVR Package Providers and Receivers
Lake Package Options Block

## Slide 31: Worked Advanced Package Transport Examples

## Slide 32: Worked Advanced Package Transport Examples
Search the examples by package type

## Slide 33: Worked Advanced Package Transport Examples
Search the examples by package type

## Slide 34
UZF/UZE
Infiltrating heat flow
Runoff heat flow
Recharging heat flow
Changes in UZ heat storage
Simulated lake temperature
LAK/LKE
Groundwater/surface-water interaction, including
convective and conductive heat exchange
Takes into account temperature of precipitation
Evaporative Cooling
Runoff heat flow
Heat from precipitation
Runoff heat flow
Recharging heat flow
Q
Evaporative cooling
Heat from precipitation
Groundwater/surface-water conductive heat exchange
Runoff heat flow
SFR/SFE
Channel routing of heat flow
Evaporative cooling
Takes into account temperature of precipitation
Groundwater/surface-water interaction, including convective and conductive heat exchange
Shallow groundwater heat flow to streams
Deep groundwater heat flow to streams
Shallow
groundwater heat flow to lakes
Deep groundwater heat flow to lakes
Simulated
stream
temperature
Runoff heat flow
Cool
Warm
Relative Cell
Temperature
UZF/UZE Routing
Groundwater/
surface-water conductive heat
exchange
Infiltrating heat flow
Advanced Package Transport